## Slide 1: [NetApp] 반도체 20년 1차 평택DB 클라우드시스템 구축 완료보고서
NetApp Korea / e-Tech system
AFF-A400 Model (MCC)

## Slide 2: NetApp AFF-A400 상세 제원
전체 모습 (캐비넷 포함) | 디스크 헤더 모습 (디스크 컨트롤러 기능 포함)
 | 디스크 확장 모듈 모습
폭(Width) : 60.9 cm
높이 (Height) : 201.4 cm (42U)
깊이 (Depth) : 128 cm
서비스 지역 : 전후방 122 cm
여유공간 : 최소 20cm 이상
A400 Header부 : 17.5cm (8U)
DS224C Disk Shelf 부 : 8.8 cm (2U)
전원 : AC 100~240 V
전류 : 30A Total
폭(Width) : 44.7 cm
높이 (Height) : 17.5 cm (4U)
깊이 (Depth) : 82.8cm
전원 : 100~240 VAC (3A,250W)
폭(Width) : 44.7 cm
높이 (Height) : 8.8 cm (2U)
깊이 (Depth) : 50.85 cm
전원 ( AC Power) : 100~240V
Controller Spec
4 x 64-bit 10-core 2.20 Ghz
Memory Size: 256 GB

## Slide 3: 전체 전력 및 발열량
metrocluster1: Site A
System Components | Qty | Rack Units | Current (Amps) |  | AC Power (Watts) |  | Thermal Rating (BTU/hr) | 
 |  |  | Typical | Worst | Typical | Worst | Typical | Worst
Brocade G610, 24-port, Enterprise, 16Gb Shortwave SFP | 2 | 2 | 0.66 | 0.78 | 120 | 146 | 410 | 498
ASA AFF A400 (2xControllers, 1xChassis) | 1 | 4 | 6.3 | 7.8 | 1,233 | 1,527 | 4,209 | 5,212
ATTO Fibre Bridge 7600N | 2 | 2 | 0.72 | 0.78 | 172 | 188 | 586.88 | 641.48
DS224C w/ 24x3.84TB SSDX357A | 3 | 6 | 1.92 | 4.26 | 372 | 834 | 1,272 | 2,847
metrocluster1: Site B
System Components | Qty | Rack Units | Current (Amps) |  | AC Power (Watts) |  | Thermal Rating (BTU/hr) | 
 |  |  | Typical | Worst | Typical | Worst | Typical | Worst
Brocade G610, 24-port, Enterprise, 16Gb Shortwave SFP | 2 | 2 | 0.66 | 0.78 | 120 | 146 | 410 | 498
ASA AFF A400 (2xControllers, 1xChassis) | 1 | 4 | 6.3 | 7.8 | 1,233 | 1,527 | 4,209 | 5,212
ATTO Fibre Bridge 7600N | 2 | 2 | 0.72 | 0.78 | 172 | 188 | 586.88 | 641.48
DS224C w/ 24x3.84TB SSDX357A | 2 | 4 | 1.28 | 2.84 | 248 | 556 | 848 | 1898

## Slide 4
NetApp AFF-A400 MCC 구성

## Slide 5: MetroCluster 구성 개요
Cluster A
Data Center A
Cluster B
Data Center B
A1
A2
HA
B1
B2
HA
B2
B1
IP
FC
SAS
ISL
컨트롤러
FC 스위치
ATTO bridge
디스크쉘프

## Slide 6: Rack 실장도
P2 전산실
P1C 전산실
NO | Model | S/N (P2전산실) | S/N (P1C전산실)
1 | DS224C (Shelf) | SHFNC2028000018 | SHFNC2025000347
2 | ATTO 7600N (Bridge) | FB7600N102251 | FB7600N102253
3 | Brocade G610 (SAN Switch) | EZL1912R010 | EZL1912R010
4 | AFF-A400 (Controller) | 452028000029 452028000030 | 452028000031 452028000032
5 | Brocade G610 (SAN Switch) | EZL1943Q01V | EZL1943Q01V
6 | ATTO 7600N (Bridge) | FB7600N102245 | FE7600M102249
7 | DS224C (Shelf) | SHFNC2025000350 | SHFNC2025000321
8 | DS224C (Shelf) | SHFNC202600030 | N/A
1
2
3
4
5
6
7
8
AFF400#2
SAN Switch x 1ea
ATTO Bridge x 1ea
SSD3.8TB x 23ea
SSD3.8TB x 23ea
SSD3.8TB x 18ea
SAN Switch x 1ea
ATTO Bridge x 1ea
metrocluster
AFF400#1
AFF400#4
SAN Switch x 1ea
ATTO Bridge x 1ea
SSD3.8TB x 14ea
SSD3.8TB x 14ea
SAN Switch x 1ea
ATTO Bridge x 1ea
AFF400#3

## Slide 7: 시스템 구성 요소
Controller 세부 정보
FC-VI
FC-VI
10G port * 2ea
10G port * 2ea
Initiator port * 4ea
Initatior port * 4ea
10G port * 4ea
10G port * 4ea
10G port * 4ea
10G port * 4ea
Site A (P2 전산실) | Site B (P1C 전산실) | 비고
16G FC = Total 12 EA | 16G FC = Total 12 EA | MCC 구성에 필요한 initiator와 FC-VI용으로 사용
10G SFP+ = Total 20 EA | 10G SFP+ = Total 20 EA | 각 Site별 iSCSI용 port는 16 사용, Peer용 4port 사용
1G MGMT = Total 2 EA | 1G MGMT = Total 2 EA | 

## Slide 8: 시스템 구성 요소
Controller – Shelf 연결
SSD Shelf
SAS to FC Switch
SAN Switch
Node
Node
SAN Switch
SAS to FC Switch
SSD Shelf
SSD Shelf
ID :20
ID :10
ID :11
ATTO 2
SAN 2
Node 2
Node 1
SAN 1
ATTO 1
SSD Shelf
SAS to FC Switch
SAN Switch
Node
Node
SAN Switch
SAS to FC Switch
SSD Shelf
ID :40
ID :30
ATTO 4
SAN 4
Node 4
Node 3
SAN 3
ATTO 3
논리적 연결
물리적 연결 (Firbe Channel)

## Slide 9: 시스템 구성 요소
스토리지 전체 구성도
VLAN1
VLAN2
192.168.51.XXX
192.168.52.XXX
VLAN1 | VLAN2 | VLAN1 | VLAN2 | VLAN1 | VLAN2 | VLAN1 | VLAN2 | VLAN1 | VLAN2 | VLAN1 | VLAN2 | VLAN1 | VLAN2 | VLAN1 | VLAN2
4a | 4b | 4c | 4d | 5a | 5b | 5c | 5d | 4a | 4b | 4c | 4d | 5a | 5b | 5c | 5d
Svm_mirror |  | Svm_unmirror |  | Svm_mirror |  | Svm_unmirror |  | Svm_mirror |  | Svm_unmirror |  | Svm_mirror |  | Svm_unmirror | 
PCI 4 |  |  |  | PCI 5 |  |  |  | PCI 4 |  |  |  | PCI 5 |  |  | 
controller#1 |  |  |  |  |  |  |  | controller#2 |  |  |  |  |  |  | 
NetApp AFF-A400 (P2)
1 port
1 port
VLAN1
VLAN2
192.168.1.XXX
192.168.2.XXX
pr-p1cz-svr-prod001
pr-p1cz-svr-prod002
pr-p1cz-svr-stb001
pr-p2z-svr-db-prod001
pr-p2z-svr-db-prod002
pr-p2z-svr-stb001
pr-p1cz-svr-dev001
pr-p1cz-svr-dev002
pr-p2z-svr-dev001
pr-p2z-svr-dev002

## Slide 10: 시스템 구성 요소
디스크 구성 정보

## Slide 11: 시스템 구성 요소
인터페이스 구성 – P2 전산실
Interface Infomations - IP |  |  |  |  |  | 
Storage Virtual Machine | Logical Interface | IPSpace | Port | Home Node | Operational Speed(Mbps) | Network address
clusterA | cluster_mgmt | Default | e0M | N1 | 1000 | 10.138.116.55
clusterA | N1_MGMT | Default | e0M | N1 | 1000 | 10.138.116.56
clusterA | N2_MGMT | Default | e0M | N2 | 1000 | 10.138.116.57
clusterA | N1_int | Default | a0a-171 | N1 | 9000 | 10.155.171.11
clusterA | N2_int | Default | a0a-171 | N2 | 9000 | 10.155.171.12
Interface Group Properties |  |  |  |  |  | 
Port Name | Node | Distribution |  |  | Create Policy | Member List
a0a-171 | N1 | IP |  |  | Single-mode | e0e, e0f
a0a-171 | N2 | IP |  |  | Single-mode | e0e, e0f
Interface Infomations - iscsi |  |  |  |  |  | 
Storage Virtual Machine | Logical Interface | Admin/Oper | Port | Home Node | Address/Mask | 
svm_mirror | m_n1_e4a | up/up | e4a-166 | N1 | 10.155.166.11/24 | 
svm_mirror | m_n1_e4b | up/up | e4b-167 | N1 | 10.155.167.11/24 | 
svm_mirror | m_n1_e5a | up/up | e5a-166 | N1 | 10.155.166.13/24 | 
svm_mirror | m_n1_e5b | up/up | e5b-167 | N1 | 10.155.167.13/24 | 
svm_mirror | m_n2_e4a | up/up | e4a-166 | N2 | 10.155.166.15/24 | 
svm_mirror | m_n2_e4b | up/up | e4b-167 | N2 | 10.155.167.15/24 | 
svm_mirror | m_n2_e5a | up/up | e5a-166 | N2 | 10.155.166.17/24 | 
svm_mirror | m_n2_e5b | up/up | e5b-167 | N2 | 10.155.167.17/24 | 
svm_unmirror | um_n1_e4c | up/up | e4c-166 | N1 | 10.155.166.12/24 | 
svm_unmirror | um_n1_e4d | up/up | e4d-167 | N1 | 10.155.167.12/24 | 
svm_unmirror | um_n1_e5c | up/up | e5c-166 | N1 | 10.155.166.14/24 | 
svm_unmirror | um_n1_e5d | up/up | e5d-167 | N1 | 10.155.167.14/24 | 
svm_unmirror | um_n2_e4c | up/up | e4c-166 | N2 | 10.155.166.16/24 | 
svm_unmirror | um_n2_e4d | up/up | e4d-167 | N2 | 10.155.167.16/24 | 
svm_unmirror | um_n2_e5c | up/up | e5c-166 | N2 | 10.155.166.18/24 | 
svm_unmirror | um_n2_e5d | up/up | e5d-167 | N2 | 10.155.167.18/24 | 
Service Processor |  |  |  |  |  | 
Node | IP | Subnet Mask |  |  | Gateway | Firmware Version
N1 | 10.138.116.58 | 255.255.255.0 |  |  | 10.138.116.1 | 13.2
N2 | 10.138.116.59 | 255.255.255.0 |  |  | 10.138.116.1 | 13.2

## Slide 12: 시스템 구성 요소
볼륨 구성 – P2 전산실
Summary Table for aggr1_N1_mirror |  |  |  |  |  |  |  |  | 
Aggregate Type | RAID Type | Disk Count | Data Disk Count | Total(GB) | Used(GB) | Available(GB) | Used(%) | No. of RAID Groups | RAID Group Size
64-bit | raid_DP, mirrored | 10 | 3 | 9,174 | 8,662 | 513 | 94% | 2 | 
Summary Table for aggr1_N2_mirror |  |  |  |  |  |  |  |  | 
Aggregate Type | RAID Type | Disk Count | Data Disk Count | Total(GB) | Used(GB) | Available(GB) | Used(%) | No. of RAID Groups | RAID Group Size
64-bit | raid_DP, mirrored | 10 | 3 | 9,174 | 8,662 | 513 | 94% | 2 | 
Summary Table for aggr2_N1_Unmirror |  |  |  |  |  |  |  |  | 
Aggregate Type | RAID Type | Disk Count | Data Disk Count | Total(GB) | Used(GB) | Available(GB) | Used(%) | No. of RAID Groups | RAID Group Size
64-bit | raid_DP, mirrored | 17 | 15 | 48,286 | 38,928 | 9,358 | 81% | 1 | 
Summary Table for aggr2_N2_Unmirror |  |  |  |  |  |  |  |  | 
Aggregate Type | RAID Type | Disk Count | Data Disk Count | Total(GB) | Used(GB) | Available(GB) | Used(%) | No. of RAID Groups | RAID Group Size
64-bit | raid_DP, mirrored | 17 | 15 | 48,286 | 38,928 | 9,358 | 81 | 1 | 
SVM | svm_mirror | (iscsi) Volume Information |  |  |  |  |  |  | 
Volume Name | Allocated | Used - Data | Used by Snapshots | Percent of Snapshots | Vol Thin Provisioned? | Security-Type | Containing Aggregate |  | 
svm_mirror | 8.40TB | 8TB | none | 0 | Volume type |  |  |  | 
svm_mirror | 8.40TB | 8TB | none | 0 | Volume type |  |  |  | 
SVM | svm_unmirror | (iscsi) Volume Information |  |  |  |  |  |  | 
Volume Name | Allocated | Used - Data | Used by Snapshots | Percent of Snapshots | Vol Thin Provisioned? | Security-Type | Containing Aggregate |  | 
svm_unmirror | 12.60TB | 12TB | none | 0 | Volume type |  |  |  | 
svm_unmirror | 12.60TB | 12TB | none | 0 | Volume type |  |  |  | 
svm_unmirror | 12.60TB | 12TB | none | 0 | Volume type |  |  |  | 
svm_unmirror | 12.60TB | 12TB | none | 0 | Volume type |  |  |  | 
svm_unmirror | 12.60TB | 12TB | none | 0 | Volume type |  |  |  | 
svm_unmirror | 12.60TB | 12TB | none | 0 | Volume type |  |  |  | 
SVM | svm_mirror | LUN Information |  |  |  |  |  |  | 
LUN Name | LUN Path | LUN Size | Space Reservation | Space allocation | 비고 |  |  |  | 
lun1 | /vol/n1_mirror_vol1/lun1 | 8TB | enabled | enabled |  |  |  |  | 
lun2 | /vol/n2_mirror_vol2/lun2 | 8TB | enabled | enabled |  |  |  |  | 
SVM | svm_unmirror | LUN Information |  |  |  |  |  |  | 
LUN Name | LUN Path | LUN Size | Space Reservation | Space allocation | 비고 |  |  |  | 
lun3 | /vol/n1_unmirror_vol3/lun3 | 12TB | enabled | enabled |  |  |  |  | 
lun4 | /vol/n1_unmirror_vol5/lun5 | 12TB | enabled | enabled |  |  |  |  | 
lun5 | /vol/n1_unmirror_vol7/lun7 | 12TB | enabled | enabled |  |  |  |  | 
lun6 | /vol/n2_unmirror_vol4/lun4 | 12TB | enabled | enabled |  |  |  |  | 
lun7 | /vol/n2_unmirror_vol6/lun6 | 12TB | enabled | enabled |  |  |  |  | 
lun8 | /vol/n2_unmirror_vol8/lun8 | 12TB | enabled | enabled |  |  |  |  | 

## Slide 13: 시스템 구성 요소
매핑 구성 – P2 전산실
LUN Mapping info |  |  | 
Vserser | LUN# | igroup | LUN ID
svm_unmirror | /vol/n1_unmirror_vol3/lun3 | pr-p1cz-svr-prod001 | 103
 | /vol/n1_unmirror_vol3/lun3 | pr-p1cz-svr-prod002 | 103
 | /vol/n1_unmirror_vol3/lun3 | pr-p1cz-svr-stb001 | 103
 | /vol/n1_unmirror_vol3/lun3 | pr-p2z-svr-db-prod001 | 103
 | /vol/n1_unmirror_vol3/lun3 | pr-p2z-svr-db-prod002 | 103
 | /vol/n1_unmirror_vol3/lun3 | pr-p2z-svr-stb001 | 103
 | /vol/n1_unmirror_vol5/lun5 | pr-p1cz-svr-dev001 | 105
 | /vol/n1_unmirror_vol5/lun5 | pr-p1cz-svr-dev002 | 105
 | /vol/n1_unmirror_vol5/lun5 | pr-p1cz-svr-stb001 | 105
 | /vol/n1_unmirror_vol5/lun5 | pr-p2z-svr-dev001 | 105
 | /vol/n1_unmirror_vol5/lun5 | pr-p2z-svr-dev002 | 105
 | /vol/n1_unmirror_vol5/lun5 | pr-p2z-svr-stb001 | 105
 | /vol/n1_unmirror_vol7/lun7 | pr-p1cz-svr-dev001 | 107
 | /vol/n1_unmirror_vol7/lun7 | pr-p1cz-svr-dev002 | 107
 | /vol/n1_unmirror_vol7/lun7 | pr-p1cz-svr-stb001 | 107
 | /vol/n1_unmirror_vol7/lun7 | pr-p2z-svr-dev001 | 107
 | /vol/n1_unmirror_vol7/lun7 | pr-p2z-svr-dev002 | 107
 | /vol/n1_unmirror_vol7/lun7 | pr-p2z-svr-stb001 | 107
 | /vol/n2_unmirror_vol4/lun4 | pr-p1cz-svr-dev001 | 104
 | /vol/n2_unmirror_vol4/lun4 | pr-p1cz-svr-dev002 | 104
 | /vol/n2_unmirror_vol4/lun4 | pr-p1cz-svr-stb001 | 104
 | /vol/n2_unmirror_vol4/lun4 | pr-p2z-svr-dev001 | 104
 | /vol/n2_unmirror_vol4/lun4 | pr-p2z-svr-dev002 | 104
 | /vol/n2_unmirror_vol4/lun4 | pr-p2z-svr-stb001 | 104
 | /vol/n2_unmirror_vol6/lun6 | pr-p1cz-svr-dev001 | 106
 | /vol/n2_unmirror_vol6/lun6 | pr-p1cz-svr-dev002 | 106
 | /vol/n2_unmirror_vol6/lun6 | pr-p1cz-svr-stb001 | 106
 | /vol/n2_unmirror_vol6/lun6 | pr-p2z-svr-dev001 | 106
 | /vol/n2_unmirror_vol6/lun6 | pr-p2z-svr-dev002 | 106
 | /vol/n2_unmirror_vol6/lun6 | pr-p2z-svr-stb001 | 106
 | /vol/n2_unmirror_vol8/lun8 | pr-p1cz-svr-dev001 | 108
 | /vol/n2_unmirror_vol8/lun8 | pr-p1cz-svr-dev002 | 108
 | /vol/n2_unmirror_vol8/lun8 | pr-p1cz-svr-stb001 | 108
 | /vol/n2_unmirror_vol8/lun8 | pr-p2z-svr-dev001 | 108
 | /vol/n2_unmirror_vol8/lun8 | pr-p2z-svr-dev002 | 108
 | /vol/n2_unmirror_vol8/lun8 | pr-p2z-svr-stb001 | 108
igroup info |  |  |  |  |  | 
Vserser | igroup | Protocol | OS | Initiators |  | 
svm_mirror | pr-p1cz-svr-prod001 | iscsi | vmware | iqn.1998-01.com.vmware:pr-p1cz-svr-prod001-3563f652 |  | 
 | pr-p1cz-svr-prod002 | iscsi | vmware | iqn.1998-01.com.vmware:pr-p1cz-svr-prod002-3c08c703 |  | 
 | pr-p1cz-svr-stb001 | iscsi | vmware | iqn.1998-01.com.vmware:pr-p1cz-svr-stb001-2064741d |  | 
 | pr-p2z-svr-db-prod001 | iscsi | vmware | iqn.1998-01.com.vmware:pr-p2z-svr-db-prod001-7adfe1ae |  | 
 | pr-p2z-svr-db-prod002 | iscsi | vmware | iqn.1998-01.com.vmware:pr-p2z-svr-db-prod002-2d48ee05 |  | 
 | pr-p2z-svr-stb001 | iscsi | vmware | iqn.1998-01.com.vmware:pr-p2z-svr-stb001-0eceda01 |  | 
igroup info |  |  |  |  |  | 
Vserser | igroup | Protocol | OS | Initiators |  | 
svm_unmirror | pr-p1cz-svr-dev001 | iscsi | vmware | iqn.1998-01.com.vmware:pr-p1cz-svr-dev001-334c477d |  | 
 | pr-p1cz-svr-dev002 | iscsi | vmware | iqn.1998-01.com.vmware:pr-p1cz-svr-dev002-7be5a356 |  | 
 | pr-p1cz-svr-prod001 | iscsi | vmware | iqn.1998-01.com.vmware:pr-p1cz-svr-prod001-3563f652 |  | 
 | pr-p1cz-svr-prod002 | iscsi | vmware | iqn.1998-01.com.vmware:pr-p1cz-svr-prod002-3c08c703 |  | 
 | pr-p1cz-svr-stb001 | iscsi | vmware | iqn.1998-01.com.vmware:pr-p1cz-svr-stb001-2064741d |  | 
 | pr-p2z-svr-db-prod001 | iscsi | vmware | iqn.1998-01.com.vmware:pr-p2z-svr-db-prod001-7adfe1ae |  | 
 | pr-p2z-svr-db-prod002 | iscsi | vmware | iqn.1998-01.com.vmware:pr-p2z-svr-db-prod002-2d48ee05 |  | 
 | pr-p2z-svr-dev001 | iscsi | vmware | iqn.1998-01.com.vmware:pr-p2z-svr-dev001-3f4d88c9 |  | 
 | pr-p2z-svr-dev002 | iscsi | vmware | iqn.1998-01.com.vmware:pr-p2z-svr-dev002-11616566 |  | 
 | pr-p2z-svr-stb001 | iscsi | vmware | iqn.1998-01.com.vmware:pr-p2z-svr-stb001-0eceda01 |  | 
LUN Mapping info |  |  |  |  |  | 
Vserser | LUN# | igroup |  | LUN ID |  | 
svm_mirror | /vol/n1_mirror_vol1/lun1 | pr-p1cz-svr-prod001 |  | 101 |  | 
 | /vol/n1_mirror_vol1/lun1 | pr-p1cz-svr-prod002 |  | 101 |  | 
 | /vol/n1_mirror_vol1/lun1 | pr-p1cz-svr-stb001 |  | 101 |  | 
 | /vol/n1_mirror_vol1/lun1 | pr-p2z-svr-db-prod001 |  | 101 |  | 
 | /vol/n1_mirror_vol1/lun1 | pr-p2z-svr-db-prod002 |  | 101 |  | 
 | /vol/n1_mirror_vol1/lun1 | pr-p2z-svr-stb001 |  | 101 |  | 
 | /vol/n2_mirror_vol2/lun2 | pr-p1cz-svr-prod001 |  | 102 |  | 
 | /vol/n2_mirror_vol2/lun2 | pr-p1cz-svr-prod002 |  | 102 |  | 
 | /vol/n2_mirror_vol2/lun2 | pr-p1cz-svr-stb001 |  | 102 |  | 
 | /vol/n2_mirror_vol2/lun2 | pr-p2z-svr-db-prod001 |  | 102 |  | 
 | /vol/n2_mirror_vol2/lun2 | pr-p2z-svr-db-prod002 |  | 102 |  | 
 | /vol/n2_mirror_vol2/lun2 | pr-p2z-svr-stb001 |  | 102 |  | 

## Slide 14: 시스템 구성 요소
인터페이스 및 Volume 구성 – P1C 전산실
Interface Infomations - IP |  |  |  |  |  | 
Storage Virtual Machine | Logical Interface | IPSpace | Port | Home Node | Operational Speed(Mbps) | Network address
clusterB | cluster_mgmt | Default | e0M | N3 | 1000 | 10.138.113.225
clusterB | N3_MGMT | Default | e0M | N3 | 1000 | 10.138.113.226
clusterB | N4_MGMT | Default | e0M | N4 | 1000 | 10.138.113.227
clusterB | N3_int | Default | a0a-171 | N3 | 9000 | 10.155.218.11
clusterB | N4_int | Default | a0a-171 | N4 | 9000 | 10.155.218.12
Interface Group Properties |  |  |  |  |  | 
Port Name | Node | Distribution |  |  | Create Policy | Member List
a0a-171 | N3 | IP |  |  | Single-mode | e0e, e0f
a0a-171 | N4 | IP |  |  | Single-mode | e0e, e0f

## Slide 15
감사합니다.