## Slide 1: [NetApp] 삼성반도체 기흥화성 DB 클라우드시스템 구축 완료보고서
NetApp Korea / e-Tech system
AFF-A400 Model (MCC)

## Slide 2: NetApp AFF-A400 상세 제원
전체 모습 (캐비넷 포함) | 디스크 헤더 모습 (디스크 컨트롤러 기능 포함)
 | 디스크 확장 모듈 모습
폭(Width) : 60.9 cm
높이 (Height) : 201.4 cm (42U)
깊이 (Depth) : 128 cm
서비스 지역 : 전후방 122 cm
여유공간 : 최소 20cm 이상
A400 Header부 : 17.5cm (8U)
DS224C Disk Shelf 부 : 8.8 cm (2U)
전원 : AC 100~240 V
전류 : 30A Total
폭(Width) : 44.7 cm
높이 (Height) : 17.5 cm (4U)
깊이 (Depth) : 82.8cm
전원 : 100~240 VAC (3A,250W)
폭(Width) : 44.7 cm
높이 (Height) : 8.8 cm (2U)
깊이 (Depth) : 50.85 cm
전원 ( AC Power) : 100~240V
Controller Spec
4 x 64-bit 10-core 2.20 Ghz
Memory Size: 256 GB

## Slide 3
NetApp AFF-A400 MCC 구성

## Slide 4: MetroCluster 구성 개요
Cluster A
Data Center A
Cluster B
Data Center B
A1
A2
HA
B1
B2
HA
B2
B1
IP
FC
SAS
ISL
컨트롤러
FC 스위치
ATTO bridge
디스크쉘프

## Slide 5: Rack 실장도
주센터
DR센터
16라인
DSR 5F
10G Switch
Brocade G610
ATTO 7600N
ATTO 7600N
AFF400A Controller
DS224C Shelf
SSD 3.8TB * 24
SSD 3.8TB * 24
SSD 3.8TB * 24
구분 | 장비 Spec
NetApp Storage | AFF400A * 4식
Expansion I/O Port | FC-VI 2Port * 8EA
Onboard I/O port | 10Gb SFP 4Port * 16EA
Expansion I/O Port | 10Gb PCI 4 Port * 16EA
SSD | SSD 3.8TB * 294EA
Backend Switch | Brocade G610 * 8식
ATTO Bridge | 7600N * 12식
SSD 3.8TB * 24
SSD 3.8TB * 24
SSD 3.8TB * 24
SSD 3.8TB * 12
SSD 3.8TB * 24
SSD 3.8TB * 24
SSD 3.8TB * 24
SSD 3.8TB * 24
10G Switch
SSD 3.8TB * 12
SSD 3.8TB * 24
SSD 3.8TB * 24
SSD 3.8TB * 14
SSD 3.8TB * 24
SSD 3.8TB * 24
SSD 3.8TB * 24
SSD 3.8TB * 16

## Slide 6: 하드웨어 정보 – BLD
구분 | 모델 | 호스트 네임 | 시리얼정보 | Console IP
스토리지 | AFF-A400 | BLD_A_N1 | 952044000403 | 12.54.207.145 (Cluster IP) 12.54.207.146
 | AFF-A400 | BLD_A_N2 | 952044000304 | 12.54.207.168
 | AFF-A400 | BLD_B_N3 | 952044000439 | 12.36.143.71 (Cluster IP) 12.36.143.72
 | AFF-A400 | BLD_B_N4 | 952044000376 | 12.36.143.73
ATTO Bridge | FibreBridge 7600N | BLD_bridge_A_1a | FB7600N102670 | 12.54.207.217
 | FibreBridge 7600N | BLD_bridge_A_1b | FB7600N102674 | 12.54.207.218
 | FibreBridge 7600N | BLD_bridge_B_1a | FB7600N102666 | 12.36.143.76
 | FibreBridge 7600N | BLD_bridge_B_1b | FB7600N102667 | 12.36.143.77
SAN Switch | BrocadeG610 | BLD_FAB_1_SW1_D5 | EZL1927R13K | 12.54.164.155
 | BrocadeG610 | BLD_FAB_2_SW2_D6 | EZL1927R12T | 12.54.164.156
 | BrocadeG610 | BLD_FAB_1_SW3_D7 | EZL1927R12X | 12.36.143.78
 | BrocadeG610 | BLD_FAB_2_SW4_D8 | EZL1927R13E | 12.36.143.79

## Slide 7: 하드웨어 정보 - PROD
구분 | 모델 | 호스트 네임 | 시리얼정보 | Console IP
스토리지 | AFF-A400 | PROD_A_N1 | 952043001221 | 12.54.207.76 (Cluster IP) 12.54.207.77
 | AFF-A400 | PROD_A_N2 | 952043001150 | 12.54.207.79
 | AFF-A400 | PROD_B_N3 | 952043001188 | 12.36.143.60 (Cluster IP) 12.36.143.61
 | AFF-A400 | PROD_B_N4 | 952043001143 | 12.36.143.62
ATTO Bridge | FibreBridge 7600N | PROD_bridge_A_1a | FB7600N102659 | 12.54.207.105
 | FibreBridge 7600N | PROD_bridge_A_1b | FB7600N102655 | 12.54.207.106
 | FibreBridge 7600N | PROD_bridge_A_1c | FB7600N102662 | 12.54.207.141
 | FibreBridge 7600N | PROD_bridge_A_1d | FB7600N102671 | 12.54.207.142
 | FibreBridge 7600N | PROD_bridge_B_1a | FB7600N102266 | 12.36.143.65
 | FibreBridge 7600N | PROD_bridge_B_1b | FB7600N102239 | 12.36.143.66
 | FibreBridge 7600N | PROD_bridge_B_1c | FB7600N102675 | 12.36.143.67
 | FibreBridge 7600N | PROD_bridge_B_1d | FB7600N102660 | 12.36.143.68
SAN Switch | BrocadeG610 | PROD_FAB_1_SW1_D5 | EZL1927R12S | 12.54.207.143
 | BrocadeG610 | PROD_FAB_2_SW2_D6 | EZL1927R12V | 12.54.207.144
 | BrocadeG610 | PROD_FAB_1_SW3_D7 | EZL1927R135 | 12.36.143.69
 | BrocadeG610 | PROD_FAB_2_SW4_D8 | EZL1927R130 | 12.36.143.70

## Slide 8: 시스템 구성 요소
Controller 세부 정보
FC-VI (16Gbps Backend FC)
iscsi-Target (10Gb Front iscsi)
MCC & Snapmirror 10GbE Network Port
FC-DISK (32Gbps Backend FC)
Cluster Mgmt 1Gbps Network Port
FibreChannel
Ethernet
2a 2b
2a 2b
1d 1c 1b 1a
1d 1c 1b 1a
4d 4c 4b 4a
4d 4c 4b 4a
e0M
e0M
e0c
5d 5c 5b 5a
5d 5c 5b 5a
e0d
e0c
e0d

## Slide 9: Cluster Inter-cluster Cabling 구성도
Controller Name | Controller Port | Controller Name | Controller Port
PROD-A-N1 / BLD-A-N1 PROD-B-N1 / BLD-B-N1 | e3a | PROD-A-N3 / BLD-A-N3 PROD-B-N3 / BLD-B-N3 | e3a
PROD-A-N2 / BLD-A-N2 PROD-B-N2 / BLD-B-N2 | e3b | PROD-A-N4 / BLD-A-N4 PROD-B-N4 / BLD-B-N4 | e3b

## Slide 10: Backend Switch Cabling (ATTO Bridge)
Fabric1 (Brocade G610-A-1 & Brocade G610-B-1)
Fabric2 (Brocade G610-A-2 & Brocade G610-B-2)
ATTO bridge-1
(SITE A-TOP)
ATTO bridge-2
(SITE A-BOTTOM)
ATTO bridge-1
(SITE B-TOP)
ATTO bridge-2
(SITE B-BOTTOM)
16라인
DSR 5F
ISL연결
ISL연결

## Slide 11: Backend Switch Cabling (FC-VI)
Fabric1 (Brocade G610-A-1 & Brocade G610-B1)
Fabric2 (Brocade G610-A-2 & Brocade G610-B2)
A-N1
A-N2
B-N3
B-N4
ISL연결
ISL연결

## Slide 12: Backend Switch Cabling (Disk Initiators)
Fabric1 (Brocade G610-A-1 & Brocade G610-B1)
Fabric2 (Brocade G610-A-2 & Brocade G610-B2)
A-N1
A-N2
B-N3
B-N4
ISL연결
ISL연결

## Slide 13: SAS Stack Cabling 구성도 - PROD
Stack | ATTO Bridge | SAS Port | Shelf ID | Shelf Port
1 | PROD_bridge_A_1a | A | 00(10) | 1 (IN)
 | PROD_bridge_A_1b | A | 00(10) | 3 (OUT)
 | PROD_bridge_A_1a | B | 01(11) | 1 (IN)
 | PROD_bridge_A_1b | B | 01(11) | 3 (OUT)
 | PROD_bridge_A_1a | C | 02(12) | 1 (IN)
 | PROD_bridge_A_1b | C | 02(12) | 3 (OUT)
2 | PROD_bridge_B_1c | A | 20(30) | 1 (IN)
 | PROD_bridge_B_1d | A | 20(30) | 3 (OUT)
 | PROD_bridge_B_1c | B | 21(31) | 1 (IN)
 | PROD_bridge_B_1d | B | 21(31) | 3 (OUT)
Stack | ATTO Bridge | SAS Port | Shelf ID | Shelf Port
1 | BLD_bridge_A_1a | A | 00(10) | 1 (IN)
 | BLD_bridge_A_1b | A | 00(10) | 3 (OUT)
 | BLD_bridge_A_1a | B | 01(11) | 1 (IN)
 | BLD_bridge_A_1b | B | 01(11) | 3 (OUT)
PROD SAS Port map
BLD SAS Port map

## Slide 14: Backend FC 구성 (FC-VI & Initiator) - BLD
System | FC Port | Configuration | Brocade G610-A1 | Brocade G610-A2
MCC-AFF400AC1-A-N1 | 2a | FC-VI (NVMIRROR) | FC0 | 
 | 2b | FC-VI (NVMIRROR) |  | FC0
 | 1d | Initiator for DISK | FC2 | 
 | 1c | Initiator for DISK |  | FC2
 | 1b | Initiator for DISK | FC3 | 
 | 1a | Initiator for DISK |  | FC3
ATTO7600N-A1 | FC1 | - | FC8 | 
 | FC2 | - |  | FC8
MCC-AFF400AC1-A-N2 | 2a | FC-VI (NVMIRROR) | FC1 | 
 | 2b | FC-VI (NVMIRROR) |  | FC1
 | 1d | Initiator for DISK | FC6 | 
 | 1c | Initiator for DISK |  | FC6
 | 1b | Initiator for DISK | FC7 | 
 | 1a | Initiator for DISK |  | FC7
ATTO7600N-A2 | FC1 | - | FC9 | 
 | FC2 | - |  | FC9
Brocade G610 | - | ISL | FC23 | FC23
Brocade G610 | - | ISL | FC24 | FC24

## Slide 15: Backend FC 구성 (FC-VI & Initiator) - PROD
System | FC Port | Configuration | Brocade G610-A1 | Brocade G610-A2
MCC-AFF400AC1-A-N1 | 2a | FC-VI (NVMIRROR) | FC0 | 
 | 2b | FC-VI (NVMIRROR) |  | FC0
 | 1d | Initiator for DISK | FC2 | 
 | 1c | Initiator for DISK |  | FC2
 | 1b | Initiator for DISK | FC3 | 
 | 1a | Initiator for DISK |  | FC3
ATTO7600N-A1 | FC1 | - | FC8 | 
 | FC2 | - |  | FC8
ATTO7600N-A2 | FC1 | - | FC9 | 
 | FC2 | - |  | FC9
MCC-AFF400AC1-A-N2 | 2a | FC-VI (NVMIRROR) | FC1 | 
 | 2b | FC-VI (NVMIRROR) |  | FC1
 | 1d | Initiator for DISK | FC6 | 
 | 1c | Initiator for DISK |  | FC6
 | 1b | Initiator for DISK | FC7 | 
 | 1a | Initiator for DISK |  | FC7
ATTO7600N-A3 | FC1 | - | FC10 | 
 | FC2 | - |  | FC10
ATTO7600N-A4 | FC1 | - | FC11 | 
 | FC2 | - |  | FC11
Brocade G610 | - | ISL | FC23 | FC23
Brocade G610 | - | ISL | FC24 | FC24

## Slide 16: Network Cabling 구성도
e0M
e0M
TO Cluster Mgmt Switch Port 1/#
TO Cluster Mgmt Switch Port 1/#
e0C,e0d
e0C, e0d
TO 10Gbp Switch Port 1/6, 1/7
TO 10Gbp Switch Port 1/6, 1/7

## Slide 17: Network Physical Configuration Overview(1)
Epuipment | Ethernet | Detail | Storage Network Port | Destination Switch
MCC-AFF400AC1-A-N1 | 10GbE ports for Storage Connectivity | 1 x 10G SFP | e0e, e0f | Pri / Sec Switch Eth1/6
MCC-AFF400AC1-A-N2 | 10GbE ports for Storage Connectivity | 1 x 10G SFP | e0e, e0f | Pri / Sec Switch Eth1/7
Total |  | 2 X 10G SFP |  | 
Equipment | Ethernet | Detail | Storage Network Port | Destination Switch
MCC-AFF400AC1-A-N1 | 1GbE ports for storage Connectivity | 1 X RJ45 | e0M | Mgmt Switch Port #/1
MCC-AFF400AC1-A-N2 | 1GbE ports for storage Connectivity | 1 X RJ45 | e0M | Mgmt Switch Port #/2
Total |  | 2 X UTP |  | 
MCC-AFF400AC1-A 장비의 10GbE MCC & Snapmirror Network port들은 Single_mode Interface 구성
Cluster Management Network
MCC & Snapmirror Network

## Slide 18: Network Physical Configuration Overview(2)
interface | Speed | Type | Role | Ifgrp | Flowcontrol
e0M | 1GbE | UTP | Node-Mgmt | - | Full
e0a | 25GbE | SFP | Cluster | - | None
e0b | 25GbE | SFP | Cluster | - | None
e0c | 1GbE | UTP | - | - | Not Configured as 1GbE Port
e0d | 1GbE | UTP | - | - | Not Configured as 1GbE Port
e0e | 10GbE | SFP | Intercluster (MCC & Snapmirror 용도) | a0a-3599 | Full
e0f | 10GbE | SFP | Intercluster (MCC & Snapmirror 용도) | a0a-3599 | Full
e0g | 10GbE | SFP | - | - | Not Configured as 10GbE Port
e0h | 10GbE | SFP | - | - | Not Configured as 10GbE Port

## Slide 19: Network / MGMT Logical Interface (Lifs) – BLD
SVM | LIF(s) | LIF role | Address/WWPN | Netmask | Default Gateway | Home Port
BLD-A400-A | cluster_MGMT | Cluster_Mgmt | 12.54.207.145 | 255.255.255.0 | 12.54.207.1 | BLD_A_N1:e0M
 | N1_MGMT | Node Mgmt | 12.54.207.146 | 255.255.255.0 | 12.54.207.1 | BLD_A_N1:e0M
 | N2_MGMT | Node Mgmt | 12.54.207.168 | 255.255.255.0 | 12.54.207.1 | BLD_A_N2:e0M
 | N1_int | intercluster | 192.168.254.51 | 255.255.255.0 | 192.168.254.1 | BLD_A_N1:a0a-3599
 | N2_int | intercluster | 192.168.254.52 | 255.255.255.0 | 192.168.254.1 | BLD_A_N2:a0a-3599
SVM | LIF(s) | LIF role | Address/WWPN | Netmask | Default Gateway | Home Port
BLD-A400-B | cluster_MGMT | Cluster_Mgmt | 12.36.143.71 | 255.255.255.0 | 12.36.143.1 | BLD_B_N3:e0M
 | N3_MGMT | Node Mgmt | 12.36.143.72 | 255.255.255.0 | 12.36.143.1 | BLD_B_N3:e0M
 | N4_MGMT | Node Mgmt | 12.36.143.73 | 255.255.255.0 | 12.36.143.1 | BLD_B_N4:e0M
 | N3_int | intercluster | 192.168.254.53 | 255.255.255.0 | 192.168.254.1 | BLD_B_N3:a0a-3599
 | N4_int | intercluster | 192.168.254.54 | 255.255.255.0 | 192.168.254.1 | BLD_B_N4:a0a-3599

## Slide 20: Network / MGMT Logical Interface (Lifs) – PROD
SVM | LIF(s) | LIF role | Address/WWPN | Netmask | Default Gateway | Home Port
PROD-A400-A | cluster_MGMT | Cluster_Mgmt | 12.54.207.76 | 255.255.255.0 | 12.54.207.1 | PROD_A_N1:e0M
 | N1_MGMT | Node Mgmt | 12.54.207.77 | 255.255.255.0 | 12.54.207.1 | PROD_A_N1:e0M
 | N2_MGMT | Node Mgmt | 12.54.207.79 | 255.255.255.0 | 12.54.207.1 | PROD_A_N2:e0M
 | N1_int | intercluster | 192.168.254.55 | 255.255.255.0 | 192.168.254.1 | PROD_A_N1:a0a-3599
 | N2_int | intercluster | 192.168.254.56 | 255.255.255.0 | 192.168.254.1 | PROD_A_N2:a0a-3599
SVM | LIF(s) | LIF role | Address/WWPN | Netmask | Default Gateway | Home Port
PROD-A400-B | cluster_MGMT | Cluster_Mgmt | 12.36.143.60 | 255.255.255.0 | 12.36.143.1 | PROD_B_N3:e0M
 | N3_MGMT | Node Mgmt | 12.36.143.61 | 255.255.255.0 | 12.36.143.1 | PROD_B_N3:e0M
 | N4_MGMT | Node Mgmt | 12.36.143.62 | 255.255.255.0 | 12.36.143.1 | PROD_B_N4:e0M
 | N3_int | intercluster | 192.168.254.57 | 255.255.255.0 | 192.168.254.1 | PROD_B_N3:a0a-3599
 | N4_int | intercluster | 192.168.254.58 | 255.255.255.0 | 192.168.254.1 | PROD_B_N4:a0a-3599

## Slide 21: Network / iscsi Logical Interface (Lifs) - BLD
SVM | LIF(s) | LIF role | Address/WWPN | Netmask | Default Gateway | Home Port
svm_BLD | n1_vl350x_iscsi_1 | Data(iscsi) | 192.168.1.47 | 255.255.255.0 | 192.168.1.1 | BLD_A_N1:e4a-3501
svm_BLD | n1_vl350x_iscsi_2 | Data(iscsi) | 192.168.2.47 | 255.255.255.0 | 192.168.2.1 | BLD_A_N1:e4b-3502
svm_BLD | n1_vl350x_iscsi_3 | Data(iscsi) | 192.168.3.47 | 255.255.255.0 | 192.168.3.1 | BLD_A_N1:e4b-3503
svm_BLD | n1_vl350x_iscsi_4 | Data(iscsi) | 192.168.4.47 | 255.255.255.0 | 192.168.4.1 | BLD_A_N1:e4b-3504
svm_BLD | n1_vl350x_iscsi_5 | Data(iscsi) | 192.168.5.47 | 255.255.255.0 | 192.168.5.1 | BLD_A_N1:e4b-3505
svm_BLD | n1_vl350x_iscsi_6 | Data(iscsi) | 192.168.6.47 | 255.255.255.0 | 192.168.6.1 | BLD_A_N1:e4b-3506
svm_BLD | n1_vl350x_iscsi_7 | Data(iscsi) | 192.168.7.47 | 255.255.255.0 | 192.168.7.1 | BLD_A_N1:e4b-3507
svm_BLD | n1_vl350x_iscsi_8 | Data(iscsi) | 192.168.8.47 | 255.255.255.0 | 192.168.8.1 | BLD_A_N1:e4b-3508
svm_BLD | n2_vl350x_iscsi_1 | Data(iscsi) | 192.168.1.48 | 255.255.255.0 | 192.168.1.1 | BLD_A_N2:e4a-3501
svm_BLD | n2_vl350x_iscsi_2 | Data(iscsi) | 192.168.2.48 | 255.255.255.0 | 192.168.2.1 | BLD_A_N2:e4a-3502
svm_BLD | n2_vl350x_iscsi_3 | Data(iscsi) | 192.168.3.48 | 255.255.255.0 | 192.168.3.1 | BLD_A_N2:e4a-3503
svm_BLD | n2_vl350x_iscsi_4 | Data(iscsi) | 192.168.4.48 | 255.255.255.0 | 192.168.4.1 | BLD_A_N2:e4a-3504
svm_BLD | n2_vl350x_iscsi_5 | Data(iscsi) | 192.168.5.48 | 255.255.255.0 | 192.168.5.1 | BLD_A_N2:e4a-3505
svm_BLD | n2_vl350x_iscsi_6 | Data(iscsi) | 192.168.6.48 | 255.255.255.0 | 192.168.6.1 | BLD_A_N2:e4a-3506
svm_BLD | n2_vl350x_iscsi_7 | Data(iscsi) | 192.168.7.48 | 255.255.255.0 | 192.168.7.1 | BLD_A_N2:e4a-3507
svm_BLD | n2_vl350x_iscsi_8 | Data(iscsi) | 192.168.8.48 | 255.255.255.0 | 192.168.8.1 | BLD_A_N2:e4a-3508

## Slide 22: Network / iscsi Logical Interface (Lifs) – BLD
SVM | LIF(s) | LIF role | Address/WWPN | Netm2ask | Default Gateway | Home Port
svm_BLD | n1_vl352x_iscsi_1 | Data(iscsi) | 192.168.21.47 | 255.255.255.0 | 192.168.21.1 | BLD_A_N1:e4a-3521
svm_BLD | n1_vl352x_iscsi_2 | Data(iscsi) | 192.168.22.47 | 255.255.255.0 | 192.168.22.1 | BLD_A_N1:e4b-3522
svm_BLD | n1_vl352x_iscsi_3 | Data(iscsi) | 192.168.23.47 | 255.255.255.0 | 192.168.23.1 | BLD_A_N1:e4b-3523
svm_BLD | n1_vl352x_iscsi_4 | Data(iscsi) | 192.168.24.47 | 255.255.255.0 | 192.168.24.1 | BLD_A_N1:e4b-3524
svm_BLD | n1_vl352x_iscsi_5 | Data(iscsi) | 192.168.25.47 | 255.255.255.0 | 192.168.25.1 | BLD_A_N1:e4b-3525
svm_BLD | n1_vl352x_iscsi_6 | Data(iscsi) | 192.168.26.47 | 255.255.255.0 | 192.168.26.1 | BLD_A_N1:e4b-3526
svm_BLD | n1_vl352x_iscsi_7 | Data(iscsi) | 192.168.27.47 | 255.255.255.0 | 192.168.27.1 | BLD_A_N1:e4b-3527
svm_BLD | n1_vl352x_iscsi_8 | Data(iscsi) | 192.168.28.47 | 255.255.255.0 | 192.168.28.1 | BLD_A_N1:e4b-3528
svm_BLD | n2_vl352x_iscsi_1 | Data(iscsi) | 192.168.21.48 | 255.255.255.0 | 192.168.21.1 | BLD_A_N2:e4a-3521
svm_BLD | n2_vl352x_iscsi_2 | Data(iscsi) | 192.168.22.48 | 255.255.255.0 | 192.168.22.1 | BLD_A_N2:e4a-3522
svm_BLD | n2_vl352x_iscsi_3 | Data(iscsi) | 192.168.23.48 | 255.255.255.0 | 192.168.23.1 | BLD_A_N2:e4a-3523
svm_BLD | n2_vl352x_iscsi_4 | Data(iscsi) | 192.168.24.48 | 255.255.255.0 | 192.168.24.1 | BLD_A_N2:e4a-3524
svm_BLD | n2_vl352x_iscsi_5 | Data(iscsi) | 192.168.25.48 | 255.255.255.0 | 192.168.25.1 | BLD_A_N2:e4a-3525
svm_BLD | n2_vl352x_iscsi_6 | Data(iscsi) | 192.168.26.48 | 255.255.255.0 | 192.168.26.1 | BLD_A_N2:e4a-3526
svm_BLD | n2_vl352x_iscsi_7 | Data(iscsi) | 192.168.27.48 | 255.255.255.0 | 192.168.27.1 | BLD_A_N2:e4a-3527
svm_BLD | n2_vl352x_iscsi_8 | Data(iscsi) | 192.168.28.48 | 255.255.255.0 | 192.168.28.1 | BLD_A_N2:e4a-3528

## Slide 23: Network / iscsi Logical Interface (Lifs) – PROD
SVM | LIF(s) | LIF role | Address/WWPN | Netmask | Default Gateway | Home Port
svm_PROD | n1_vl350x_iscsi_1 | Data(iscsi) | 192.168.1.45 | 255.255.255.0 | 192.168.1.1 | PROD_A_N1:e4a-3501
svm_PROD | n1_vl350x_iscsi_2 | Data(iscsi) | 192.168.2.45 | 255.255.255.0 | 192.168.2.1 | PROD_A_N1:e4b-3502
svm_PROD | n1_vl350x_iscsi_3 | Data(iscsi) | 192.168.3.45 | 255.255.255.0 | 192.168.3.1 | PROD_A_N1:e4b-3503
svm_PROD | n1_vl350x_iscsi_4 | Data(iscsi) | 192.168.4.45 | 255.255.255.0 | 192.168.4.1 | PROD_A_N1:e4b-3504
svm_PROD | n1_vl350x_iscsi_5 | Data(iscsi) | 192.168.5.45 | 255.255.255.0 | 192.168.5.1 | PROD_A_N1:e4b-3505
svm_PROD | n1_vl350x_iscsi_6 | Data(iscsi) | 192.168.6.45 | 255.255.255.0 | 192.168.6.1 | PROD_A_N1:e4b-3506
svm_PROD | n1_vl350x_iscsi_7 | Data(iscsi) | 192.168.7.45 | 255.255.255.0 | 192.168.7.1 | PROD_A_N1:e4b-3507
svm_PROD | n1_vl350x_iscsi_8 | Data(iscsi) | 192.168.8.45 | 255.255.255.0 | 192.168.8.1 | PROD_A_N1:e4b-3508
svm_PROD | n2_vl350x_iscsi_1 | Data(iscsi) | 192.168.1.46 | 255.255.255.0 | 192.168.1.1 | PROD_A_N2:e4a-3501
svm_PROD | n2_vl350x_iscsi_2 | Data(iscsi) | 192.168.2.46 | 255.255.255.0 | 192.168.2.1 | PROD_A_N2:e4a-3502
svm_PROD | n2_vl350x_iscsi_3 | Data(iscsi) | 192.168.3.46 | 255.255.255.0 | 192.168.3.1 | PROD_A_N2:e4a-3503
svm_PROD | n2_vl350x_iscsi_4 | Data(iscsi) | 192.168.4.46 | 255.255.255.0 | 192.168.4.1 | PROD_A_N2:e4a-3504
svm_PROD | n2_vl350x_iscsi_5 | Data(iscsi) | 192.168.5.46 | 255.255.255.0 | 192.168.5.1 | PROD_A_N2:e4a-3505
svm_PROD | n2_vl350x_iscsi_6 | Data(iscsi) | 192.168.6.46 | 255.255.255.0 | 192.168.6.1 | PROD_A_N2:e4a-3506
svm_PROD | n2_vl350x_iscsi_7 | Data(iscsi) | 192.168.7.46 | 255.255.255.0 | 192.168.7.1 | PROD_A_N2:e4a-3507
svm_PROD | n2_vl350x_iscsi_8 | Data(iscsi) | 192.168.8.46 | 255.255.255.0 | 192.168.8.1 | PROD_A_N2:e4a-3508

## Slide 24: Network / iscsi Logical Interface (Lifs) – PROD
SVM | LIF(s) | LIF role | Address/WWPN | Netm2ask | Default Gateway | Home Port
svm_PROD | n1_vl352x_iscsi_1 | Data(iscsi) | 192.168.21.45 | 255.255.255.0 | 192.168.21.1 | PROD_A_N1:e4a-3521
svm_PROD | n1_vl352x_iscsi_2 | Data(iscsi) | 192.168.22.45 | 255.255.255.0 | 192.168.22.1 | PROD_A_N1:e4b-3522
svm_PROD | n1_vl352x_iscsi_3 | Data(iscsi) | 192.168.23.45 | 255.255.255.0 | 192.168.23.1 | PROD_A_N1:e4b-3523
svm_PROD | n1_vl352x_iscsi_4 | Data(iscsi) | 192.168.24.45 | 255.255.255.0 | 192.168.24.1 | PROD_A_N1:e4b-3524
svm_PROD | n1_vl352x_iscsi_5 | Data(iscsi) | 192.168.25.45 | 255.255.255.0 | 192.168.25.1 | PROD_A_N1:e4b-3525
svm_PROD | n1_vl352x_iscsi_6 | Data(iscsi) | 192.168.26.45 | 255.255.255.0 | 192.168.26.1 | PROD_A_N1:e4b-3526
svm_PROD | n1_vl352x_iscsi_7 | Data(iscsi) | 192.168.27.45 | 255.255.255.0 | 192.168.27.1 | PROD_A_N1:e4b-3527
svm_PROD | n1_vl352x_iscsi_8 | Data(iscsi) | 192.168.28.45 | 255.255.255.0 | 192.168.28.1 | PROD_A_N1:e4b-3528
svm_PROD | n2_vl352x_iscsi_1 | Data(iscsi) | 192.168.21.46 | 255.255.255.0 | 192.168.21.1 | PROD_A_N2:e4a-3521
svm_PROD | n2_vl352x_iscsi_2 | Data(iscsi) | 192.168.22.46 | 255.255.255.0 | 192.168.22.1 | PROD_A_N2:e4a-3522
svm_PROD | n2_vl352x_iscsi_3 | Data(iscsi) | 192.168.23.46 | 255.255.255.0 | 192.168.23.1 | PROD_A_N2:e4a-3523
svm_PROD | n2_vl352x_iscsi_4 | Data(iscsi) | 192.168.24.46 | 255.255.255.0 | 192.168.24.1 | PROD_A_N2:e4a-3524
svm_PROD | n2_vl352x_iscsi_5 | Data(iscsi) | 192.168.25.46 | 255.255.255.0 | 192.168.25.1 | PROD_A_N2:e4a-3525
svm_PROD | n2_vl352x_iscsi_6 | Data(iscsi) | 192.168.26.46 | 255.255.255.0 | 192.168.26.1 | PROD_A_N2:e4a-3526
svm_PROD | n2_vl352x_iscsi_7 | Data(iscsi) | 192.168.27.46 | 255.255.255.0 | 192.168.27.1 | PROD_A_N2:e4a-3527
svm_PROD | n2_vl352x_iscsi_8 | Data(iscsi) | 192.168.28.46 | 255.255.255.0 | 192.168.28.1 | PROD_A_N2:e4a-3508

## Slide 25: DISK / RAID Configuration
Aggregate 구성 - BLD |  |  |  | 
Node Name | Aggr Name | Raid Type | Raid Groups | Usable 용량
BLD_A_N1 | aggr0_N1_root | RAID_DP (64bit) | 2x RIAD group of 3x 3.8TB SSD | Controller OS (Mirrored)
 | aggr1_N1_data | RAID_DP (64bit) | 2x RIAD group of 10x 3.8TB SSD | 23.78 TiB (Mirrored)
BLD_A_N2 | aggr0_N2_root | RAID_DP (64bit) | 2x RIAD group of 3x 3.8TB SSD | Controller OS (Mirrored)
 | aggr1_N2_data | RAID_DP (64bit) | 2x RIAD group of 10x 3.8TB SSD | 23.78 TiB (Mirrored)
Aggregate 구성 - PROD |  |  |  | 
Node Name | Aggr Name | Raid Type | Raid Groups | Usable 용량
PROD_A_N1 | aggr0_N1_root | RAID_DP (64bit) | 2x RIAD group of 3x 3.8TB SSD | Controller OS (Mirrored)
 | aggr1_N1_data | RAID_DP (64bit) | 2x RIAD group of 44x 3.8TB SSD | 120.7 TiB (Mirrored)
PROD_A_N2 | aggr0_N2_root | RAID_DP (64bit) | 2x RIAD group of 3x 3.8TB SSD | Controller OS (Mirrored)
 | aggr1_N2_data | RAID_DP (64bit) | 2x RIAD group of 44x 3.8TB SSD | 120.7 TiB (Mirrored)

## Slide 26: Volume Configuration - BLD
Name | Aggreagte | Size | Snapshot Reserve | Volume Thin or Thick Provisioned | efficiency | Snapshot Policy
n1_data1 | aggr1_N1_data | 16.81 TB | 0 % | Thick | Disabled | none
n2_data2 | aggr1_N2_data | 13.67 TB | 0 % | Thick | Disabled | none

## Slide 27: Volume Configuration - PROD
Name | Aggreagte | Size | Snapshot Reserve | Volume Thin or Thick Provisioned | efficiency | Snapshot Policy
n1_data01 | aggr1_N1_data | 16.81 TB | 0 % | Thick | Disabled | none
n1_data02 | aggr1_N1_data | 16.81 TB | 0 % | Thick | Disabled | none
n1_data03 | aggr1_N1_data | 16.81 TB | 0 % | Thick | Disabled | none
n1_data04 | aggr1_N1_data | 16.81 TB | 0 % | Thick | Disabled | none
n1_data05 | aggr1_N1_data | 16.81 TB | 0 % | Thick | Disabled | none
n1_data06 | aggr1_N1_data | 16.81 TB | 0 % | Thick | Disabled | none
n1_data07 | aggr1_N1_data | 16.81 TB | 0 % | Thick | Disabled | none
n2_data08 | aggr1_N2_data | 16.81 TB | 0 % | Thick | Disabled | none
n2_data09 | aggr1_N2_data | 16.81 TB | 0 % | Thick | Disabled | none
n2_data10 | aggr1_N2_data | 16.81 TB | 0 % | Thick | Disabled | none
n2_data11 | aggr1_N2_data | 16.81 TB | 0 % | Thick | Disabled | none
n2_data12 | aggr1_N2_data | 16.81 TB | 0 % | Thick | Disabled | none
n2_data13 | aggr1_N2_data | 16.81 TB | 0 % | Thick | Disabled | none
n2_data14 | aggr1_N2_data | 5.25 TB | 0 % | Thick | Disabled | none

## Slide 28: LUNs Configuration - BLD
Aggr Name | Volume Name | LUN Name | Protocol | Size | space-reserve | space-allocation | LUN Mapping | LUN ID
aggr1_N1_data | n1_data1 | /vol/n1_data1/lun1 | iscsi | 16 TB | enabled | enabled | Host 24대 | 1
aggr1_N2_data | n2_data2 | /vol/n2_data2/lun2 | iscsi | 13 TB | enabled | enabled |  | 2

## Slide 29: LUNs Configuration – PROD
Aggr Name | Volume Name | LUN Name | Protocol | Size | space-reserve | space-allocation | LUN Mapping | LUN ID
n1_data01 | aggr1_N1_data | /vol/n1_data01/lun01 | iscsi | 16 TB | enabled | enabled | Host 78대 | 1
n1_data02 | aggr1_N1_data | /vol/n1_data02/lun02 | iscsi | 16 TB | enabled | enabled |  | 2
n1_data03 | aggr1_N1_data | /vol/n1_data03/lun03 | iscsi | 16 TB | enabled | enabled |  | 3
n1_data04 | aggr1_N1_data | /vol/n1_data04/lun04 | iscsi | 16 TB | enabled | enabled |  | 4
n1_data05 | aggr1_N1_data | /vol/n1_data05/lun05 | iscsi | 16 TB | enabled | enabled |  | 5
n1_data06 | aggr1_N1_data | /vol/n1_data06/lun06 | iscsi | 16 TB | enabled | enabled |  | 6
n1_data07 | aggr1_N1_data | /vol/n1_data07/lun07 | iscsi | 16 TB | enabled | enabled |  | 7
n2_data08 | aggr1_N2_data | /vol/n2_data08/lun08 | iscsi | 16 TB | enabled | enabled |  | 8
n2_data09 | aggr1_N2_data | /vol/n2_data09/lun09 | iscsi | 16 TB | enabled | enabled |  | 9
n2_data10 | aggr1_N2_data | /vol/n2_data10/lun10 | iscsi | 16 TB | enabled | enabled |  | 10
n2_data11 | aggr1_N2_data | /vol/n2_data11/lun11 | iscsi | 16 TB | enabled | enabled |  | 11
n2_data12 | aggr1_N2_data | /vol/n2_data12/lun12 | iscsi | 16 TB | enabled | enabled |  | 12
n2_data13 | aggr1_N2_data | /vol/n2_data13/lun13 | iscsi | 16 TB | enabled | enabled |  | 13
n2_data14 | aggr1_N2_data | /vol/n2_data14/lun14 | iscsi | 5 TB | enabled | enabled |  | 14

## Slide 30
감사합니다.